## Slide 1: 신호 최적화 최종발표
ETRI연구연수생 강민수

## Slide 2: Contents
Current Model
  3x3Grid Single-Agent Model without Constraints(Depreciated)
  3x3Grid Decentralized Model without Constraints(Depreciated)
  3x3Grid/Dunsan Decentralized Model with Practical Constraints
  Dunsan Decentralized CNN/CNN-reduced Model with Practical Constraints
Upcoming Model
  Continuous Action Model with Practical Constraints

## Slide 3: 3x3Grid Single-Agent/Decentralized Model without Constraints(Depreciated)
Condition (seed fixed)
  Generating probability 0.133 (left, right), 0.388 (up, down)
  Restricted direction of vehicles(via)/Not restricted direction(no via)
  Central agent(n_1_1), 9 Agents(decentralized)
State
  The number of inflow vehicles from each inflow edge(left, straight)
Action
  Deciding next phase(without an order), every 20s (with all yellow 3 seconds)
Reward
  Penalty on Pressure (= inflow-outflow)

## Slide 4: Comparison between Simulation & Single Agent
Simulation 0.133 (left, right), 0.388 (up, down), phase 42(G), 3(Y)
  The number of arrived number: 8295 (no via), 8794 (via)
Experiment(Single-Agent Model)
  The number of average arrived number: 9060 (no via), 9281 (via)
Agent
5~8% Increase
300m

## Slide 5: Comparison between Simulation & Decentralized Agents
Simulation 0.133 (left, right), 0.388 (up, down), phase 20(G), 3(y)
  The number of arrived number: 9474 (no via), 9765(via)
Experiment(Decentralized Agents Model)
  The number of avg arrived number: 10600(no via, blue), 10800 (via, orange)
10~11% Increase

## Slide 6: 3x3Grid/Dunsan Decentralized Model with Practical Constraints
Condition(seed fixed)
  Random routing vehicle generation (period 0.8), scale 1.1 (by randomTrips.py)
  9 Decentralized Agents(No offsets, Update Asynchronously)
  4 Phases(Vertical/Horizontal straight and left) 37s each, followed by all yellow 3s
  Model applied min/max duration(28s,49s) and phase period(160s)
State
  The number of inflow vehicles from each inflow edge(left, straight)
  Update phase demand(# of vehicles inflow) from end of phase period

## Slide 7: 3x3Grid/Dunsan Decentralized Model with Practical Constraints
Condition(seed fixed)
  Real Demand(0-3[scaled 2times],7-10am[scaled 0.7 times])
  9 Decentralized Agents(Update asynchronously by offsets)
  Using Each designated phase rule in xml file
  Model learned from only first 3600 steps
State
  The number of inflow vehicles from each edge(left, straight)
  Update demand(# of vehicles inflow) from end of phase period
Turn off the Signal
Controlling Sector

## Slide 8: 3x3Grid/Dunsan Decentralized Model with Practical Constraints
Agent
  Decentralized DQN, Soft Target Update(Tau: 0.001)
  Common phase-based ratio discrete distribution
  2 Actions/agent = time action, rate action
  Action Space
    Time action space:
    Rate action space: 17, distributing time to each phase ex) [0,1,0,-1],[0,0,0,0],[1,1,-1,-1]
Reward
  Reward= -Pressure = (inflow HaltingNumber – outflow VehicleNumber)
  If action is beyond the threshold(min/max duration), give penalties
  Update end of each phase
# of phase | Action space
2 | 2
3 | 3C2*2+1
4 | 4C2*2+4C4*4+1
5 | 5C2*2+5C4*4+1
Dunsan Rate Action

## Slide 9: Decentralized Model with Practical Constraints
RL Modeling
Environment
Traci
Neural Net (shared params)
Agent
Agent
Agent
Agent
Action:
Update Mask
TL_Period
Reward:
State:

## Slide 10: Decentralized Model with Practical Constraints
DNN Modeling
Vehicle Info from Traci
Left Straight
Inflow Demand
Intersection Traffic Demand
Concatenated
Traffic Demand
Super Q Network
Time Q Network
Rate Q Network
Neural Net (Shared Params)
argmaxQ = rate action
argmaxQ = time action
# of phase | Action space
2 | 2
3 | 7
4 | (4C2)*2+4+1
5 | 5C2+5C4+1
Other Agents

## Slide 11: Decentralized Model with Practical Constraints
3x3 grid
  9 Agents
  Random Routing Generation  1 period, 1.5 scaled
Dunsan
  11 Agents
  Real Demand based training  0-3am, 2.0 scaled
Avg Value | Simulation | Decentralized
Travel Time (per edge) | 13.82s | 14.52
Velocity | 5.93m/s | 5.769m/s
Waiting Time (whole trip) | 495.5s/veh | 534.1s/veh
Arrived Num | 10951 | 10863
Avg Value | Simulation | Decentralized
Travel Time (per edge) | 61.0s | Not converged
Velocity | 3.43m/s | -
Waiting Time (whole trip) | 40.2s/veh | -

## Slide 12: Dunsan Decentralized CNN/CNN-reduced Model with Practical Constraints
CNN based Decentralized Model
  CNN: Convolution Neural Network
    Feature extraction in selected region  Apply to intersection information
    Advantage: less parameters than Fully Connected Network  Lightweighting
  CNN based Model (Feature Extraction) 1000epochs
    Current Channel: 8 (zero-padded demand of vehicles from inflow edge)
    After CNN, the number of channel: 16
    Learning Time: 8h 11m(0-3am), 30h(7-10am)
  CNN based Lightweight Model
    By using Conv1d, dimensionality reduced to 1 channel with feature
    Learning Time: 6h 10m, 26h(7-10am)

## Slide 13: Dunsan Decentralized CNN/CNN-reduced Model with Practical Constraints
CNN based model(Single Agent based Model)
Vehicle Info from Traci
Left Demand Straight Demand
Inflow Demand (Zero Padded)
Intersection Traffic Demand
Concatenated
Traffic Demand
Super Q Network
Time Q Network
Rate Q Network
Neural Net (Shared Params)
argmaxQ = rate action
argmaxQ = time action
Conv1d
8 Activation Maps/
1 Activation Map
Other Agents
Other Agents

## Slide 14: Analysis of Decentralized CNN-reduced Model
CNN Model(0to3am)
  8 feature  Checking demand change
CNN-reduced Model(0to3am)
  1 feature  Current traffic info
Avg Value(interest edges) | Simulation | Decentralized-CNN | Decentralized-CNN-reduced
Travel Time (per edge) | 33.8s | 47.5s | 42.4s
Avg Velocity(edge veh) | 5.99m/s | 5.52m/s | 5.82m/s
Waiting Time (during whole trip) | 165.1s/edg | 210s/edg | 175.5s/edg
Arrived Num (all edge) | 11167 | 11022 (02-19_09-29-17) | 11114 (02-23_09-36-26)
Travel Time: mean value of getTraveltime for all steps that are filtered less than two tl periods
Avg Velocity: average velocity from edge that defined to control by model

## Slide 15: Analysis of Decentralized CNN-reduced Model
Avoiding Overfitting(Validation)
  Add Dropout Layer between fully connected layer in super Q Network
  Apply peak demand(7-10am) to the model learned from free demand(0-3am)
Conclusion: For wide coverage, strengthen performance by dropout layer
Avg Value | Simulation | Before adding dropout | After adding dropout
Travel Time (per edge) | 43.546s | 54.716s | 44.5s
Velocity(edge veh) | 5.413m/s | 5.187m/s | 5.46m/s
Waiting Time (count all veh in edg) | 208.95s/edg | 287.42s/edg | 219.54s/edg
Arrived Num | 12111 | 11873 | 12175(02-24_15-20-23)

## Slide 16: Analysis of Decentralized CNN-reduced Model
Practical Constraints without minimum of duration condition
  Removing penalty in action that is less/more than min/maximum length of duration
  Purpose: Verifying whether regulations lead traffic jam or not
  Learning process and Reward comparison
Conclusion: 1) Current signal is incomplete (scope to improve more) 2) Hard to learn model with constraint 3) Arbitrary Penalty -> Not converge
 | Learning with Constraint | Learning without Constraint
Learning Time | 6h 14m | 5h 56m
Avg converge reward | 9.2e-3(02-25_08-50-45,not converge yet) | -8.8e-3(02-24_15-20-23)
Avg velocity(sim in 7-10) | 5.40m/s | 5.46m/s

## Slide 17: Final Model
Decentralized CNN-reduced Deep Reinforcement Learning model
  Hyperparameters: tau 0.001, gamma 0.99, lr 1e-4, eps 0.8, both decay_rate 0.99, batch 64
Vehicle Info from Traci
Left Demand Straight Demand
Inflow Demand (Zero Padded)
Intersection Traffic Demand
Concatenated
Traffic Demand
Super Q Network
Linear(Num_agent,48,36)
Dropout(0.4,0.3)
Time Q Network
(36,24,time_action)
Rate Q Network
(36,24,rate_action)
Neural Net (Shared Params)
argmaxQ = rate action
argmaxQ = time action
Conv1d
(1,)
1 Activation Map
(num_phase,4,1)
Other Agents
Other Agents

## Slide 18: Reason for failing experiment
Generated Actual data biased for fixed time signal control
Congested road conditions not being reflected by scaled data
  Using 7-10am demand instead of 0-3am
  Trade off between learning time(x3 in 7-10) and performance
Hard to improve the performance due to fixed offset value
Due to lack of other traffic light control, lead RL traffic lights lower performance
No convergence due to arbitrary penalty in case of exceeding threshold(min/max duration)
In SUMO, road deletions due to absence of pocket(left turn) lead unintended traffic jam
Traffic Jam Sector
RL Controlling Sector

## Slide 19: Continuous Action Model with Practical Constraints
DDPG based Model
  Current action space: Time, Rate  Phase length (for each phase)
  Splitting rest of time (Total TL period – sum of min durations for each phase)
  Phase distribution by the results of softmax()
    Sum of results by softmax function = 1  Easy to distribute length of phase
Min Duration
Action
DDPG target
Actor
Critic
Environment
State
Update, Approx.
DDPG
Actor
Critic
Soft Update

## Slide 20: Thank you