## Slide 1: 사전 발표
강민수

## Slide 2: 목표
교통 공학 용어 정리 및 학습
SUMO Network 제작 TraCI 함수
강화학습 내용 파악
논문 Review
State, Reward, Action 종류 판별
개선점

## Slide 3: Preliminary
TOD Control (Time of Day), Pre-time, Fix time
  1일 시간대 별로 사용자가 입력한 신호 시간에 따라 매일 반복하여 신호를 제어하는 것
  장점
    안정된 도로에서 효율이 높고, 요일 별 혹은 일 별 교통 변동량이 적으면 효율적
  단점
    복잡한 도로에서 효율이 낮음
    사용자의 사전 조사 및 검증이 필요
  적합 주기, 녹색 시간, Offset을 준비한 후 설정된 신호 시간으로 운영
  가로 축, 지역 별로 유사 교통 패턴을 갖는 경우 ‘교차로 group’ 편성

## Slide 4: Preliminary
Considering factors when constructing traffic system
  신호 교차로간 거리
    짧을 수록 연동 시스템의 구축 필요성 높음
    멀면 분산효과가 커서 필요성이 낮음
  도로 운영
    일방 통행, 양방 통행  양방이 운영하기 어려움, 공통적으로 신호등이 없는 횡단보도는 문제임(offset 설정 문제)
  접근로의 상태
    이상적인 경우: 교차로간 거리와 주행속도만으로 offset decision 가능
    현실적인 경우: 불법 주정차, 중간 유입 차량, outflow 차량 모두 고려해야 함
  차량의 도착 특성
    도착율이 일정한 경우, 연동 필요가 없음
  시간에 따른 교통량 변화
    첨두 시간대: 연동 시스템의 구축보다 통과용량 극대화
    비 첨두 시간대: 두 교차로 사이에 유입되는 간선도로가 없을 때

## Slide 5: Preliminary
Spill back
  신호교차로에서 꼬리물기, 교통량 과다 등이 원인이 되어 inflow intersection까지 차량이 넘쳐나서 원활한 통행을 방해하는 현상
Signal Phase
  Signal set in intersection (n lane->n*4 signal set length)
  보통 8개의 Signal phase를 가짐 (Combined with movement signal)
  Isolated intersection에서는 paired-signal phases를 주로 사용
  Multi-grouped intersection에서는 single-signal phase 사용하여 spill back 예방

## Slide 6: SUMO Network 제작
2x2 grid
3x3 grid

## Slide 7: TraCI
Additional file 을 이용하여 Traffic Light를 조절 -.add.xml format 사용
Phase Setting - setPhase function
Duration Setting - setPhaseDuration
Complete Program Setting: Static signal Plan - setProgramLogic

## Slide 8: Defining New TLS-Programs
Additional file을 사용  tlLogic id를 부여하여 사용함(.nod.xml에서 부여한 id와 동일할 때, 동작함)
Program ID는 ‘off’를 제외하고 부여
아래 Character는 소문자는 decelerate 함을 의미(set할 때, 기준)
설명
Red Light, 이 신호일 때, junction에서 차량이 정지하면 Teleport
Yellow Light, 차량이 Junction에서 멀면 deceleration, 아니면 pass
Green Light with no priority, 비 보호 녹색 신호, 먼저 온 priority signal 수신 차량이 있는 경우 deceleration
Green Light with priority, junction을 우선 pass하는 신호
Green Right-turn arrow, junction type ‘traffic_light_right_on_red’에서만 생성되며, priority가 대향 방향 차량이 갖는 경우 정지
Red+yellow, Red에서 Green으로 바뀌기 전의 노란색 신호, 차량이 출발안함
깜박이면 차량이 양보해야함을 의미하는 신호
차량에게 통행권이 있는 신호

## Slide 9: Defining New TLS-Programs
TLS state 부여 방식 - 순서대로 부여하되, lane의 방향 별로 부여 - 0번에서 총 7가지 state가 존재
Junction 형태 설정시 개수 조절 가능
Connection 설정으로 Merge 형태 조절 가능
0
1
2
3

## Slide 10: Traffic State, Action
Traffic Lights Value Retrieval - ID list: getIDList - State: getRedYellowGreenState - Phase duration: getPhaseDuration, - Current phase: getPhase 함수, 현재 phase의 index - Complete program definition: getCompleteRedYellowGreenDefinition, TL 프로그램 받아오기
Change Traffic Lights State - Change state: setRedYellowGreenState - Change phase duration: setPhaseDuration - Complete program definition: setCompleteRedYellowGreenDefinition, 새로운TL 프로그램 삽입 - Change program logic: setProgramLogic : logic 삽입

## Slide 11: Traffic Observation Data
Induction Loops detector (TraCI)
  Induction Loop value retrieval
    ID List: getIDList
    # Visiting Vehicle: getLastStepVehicleNumber
    Percentage of time that was occupied: getLastStepOccupancy
Lane Area detector (TraCI)
  Lane Area detector value retrieval
    ID List: getIDList
    # Visiting Vehicle: getLastStepVehicleNumber
    Percentage of time that was occupied: getLastStepOccupancy

## Slide 12: Toward A Thousand Lights: Decentralized Deep Reinforcement Learning for Large-scale Traffic Signal Control
ETRI 연수생 강민수

## Slide 13: Contents
Motivation - Reinforcement Learning을 Traffic System에 적용하기 위해 필요한 조건 - 지금까지 적용이 어려웠던 이유
Related Work - Conventional Transportation Method and Max pressure control - RL- based approach and their challenge
Approach - Super agent based multi-intersection method with FRAP model
Result
Comment - Improvement proposal

## Slide 14: Motivation
Traffic congestion
  Led by rapid urbanization
  Increase emission gas (contributes 23% of total CO2 emission) 40% of total vehicle emissions generated by traffic system  Trend: applying RL method for traffic signal control
Traditional transportation approaches
  Pre-timed control: Deciding traffic signal plan that change according to the real-time data
  Actuated control: Pre-defined rules and real-time data-based method that is affected by queue length
  Adaptive control: current traffic situation(deciding a best signal plan for current situation from sensors)
  Optimization-based control: Relying less human knowledge and deciding the plans by observed data  Given traffic model and pre-defined rule  Fail to adjust to dynamic traffic

## Slide 15: Motivation
Challenge
  To control and coordinate traffic lights in large-scale urban network  Highly correlated due to densely connected
  Traditional Method is not well adjusted when the traffic is dynamic
3 Key Issues to handle the challenge by RL method
  Scalability: learn effectively on a large scale, and the global optimization goal simultaneously
  Coordination: Optimizing signal timing for TL jointly when in proximity
  Data feasibility: Not use the data that are hard to occur when learning by the RL-based method

## Slide 16: Related work
Conventional Transportation Methods for multi-intersection control
  Same cycle length
  Facilitated traffic of selected movement: modifying the offset between consecutive intersection  Problem of this approach
        Few network are only uniform for simple approach (Small grid network -> fixed offset achieve coordination)
        Difficult to provide a global optimization
Start from here
When arrive this point, turn on the green light

## Slide 17: Related work
Max Pressure : optimization-based method
  Providing global optimization through coordination
  Developed to optimize the global vehicle travel time, throughput and # of stops at intersections  Challenges
        Still rely on assumptions of simple traffic condition, HARD to apply to real world
RL-based single-intersection methods
  Outstanding performance over conventional transportation methods
  For satisfying scalability,  Advance to ‘RL-based multi-intersection methods’
Pressure change
from NS to EW
MaxPressure (Varaiya 2013; Kouvelas et al. 2014)

## Slide 18: Related work
Reinforcement Learning(RL) based multi-intersection methods
  Treat all the intersection separately and apply individual traffic signal control
    Scale-up easily
    Cannot coordinate with neighbors, achieve their own goals
  Centralized optimization over multiple coordinated agents
    Achieve coordination with neighbor intersections
    Network scale expands, optimization is infeasible due to large joint action space
 Trade-off between scalability and coordination
Intellilight, Wei,H.;Zheng,G.;Yao,H.;andLi,Z. 2018.
Colight, Wei, H.; Xu, N.; and Li, Z. 2019b.

## Slide 19: Related work
Issues that are hard to apply RL in large-scale network
  Uni-intersection related reward system
  Few reward design for direct coordination
  Current RL method includes infeasible features in the states
Decentralized Approach based on RL
  Considering both scalability and coordination
  Decentralized agent network

## Slide 20: Approach
MPLight
  Utilizing simple features that are feasible in the real world <- overcome infeasibility
  Sharing parameters of intersections <- overcome scalability
    Not sharing all the parameters naively  inferior performance because of having different structures each
    Not applying the control of large flow to the system with little traffic - Following similar control logic and enhancing the speed of learning by sharing their learned knowledge - base model, ‘FRAP’
  Integrating the concept of “pressure” into reward design for coordination
    Derived from ‘max pressure control theory’, aimed at the global throughput in the area
    Balancing the distribution of vehicle by minimizing the pressure and maximizing the throughput - pressure: discrepancy of the number of vehicles inflow and outflow
  Decentralized agent based on Deep Q-Network <- overcome coordination

## Slide 21: Approach: FRAP
FRAP architecture(base model)
  Flipping and Rotation and considers All phase Configuration
  Focus on the relation between different traffic movement
    Reduction of exploration space by rotating and flipping
    Current model need 8phases experience to learn in the same state  By rotating and flipping, Reduces needed experience in 1/8 scale
  Adapting different intersection structure easily by two principles
    Principles of competition: Larger traffic indicates higher demand for ‘green’
    Principles of invariance: signal control should be invariant to symmetries such as rotating and flipping
  Prediction of phase score into tree stages(for traffic movement)
    Phase demand modeling: features from both current phase and # of vehicles through 2 fc-layers
    Phase pair representation: the score of a phase depends on its competition with the other phase
    Phase pair competition: predicted score of a phase over all its opponents

## Slide 22: Approach: FRAP
FRAP Network (Prediction of phase score into three stages)
Competing Phase Demand
# of vehicles
Current phase
Phase demand
Check Conflicting

## Slide 23: Approach: DQN
Deep Q-Network
  Value-based learning(Q learning), Epsilon-greedy
  Loss function that compare fixed target Q and approximated local Q
  Soft update the target Q network() periodically
  Use experience replay for updating Q - Using on-policy make the data highly correlated  by using replay, uniformly random sample - Disadvantage: using much memory during the learning

## Slide 24: Approach: DQN Agent
Reinforcement Learning Structure(Deep Q-Network)
  Observation
    Current phase
    Pressure of the 12 traffic movements - fewer movements -> zero-padded
  Action(every 10s)
    Choose phase among the 8 candidate phases  Not choosing all the phase
    Select the phase based on Max Pressure Control Law(FRAP)
  Reward
    Difference between the sum of queueing vehicles inflows and the sum of queueing vehicles outflow  by maximizing the reward, agent will try to stabilize
Super Agent
Agents

## Slide 25: Approach: DQN Agent & Setting
Parameter Sharing
  All parameters shared among all the agents (Observation data sharing)  One intersection can get data from all the other intersections’ experience replay
Setting (Synthetic data on a 4x4 network)
  After the designated phase, 3s yellow signal and 2s all red time are followed
  Bi-directional and dynamic flows - Flat(=0.6) - Peak(=0.3)
  Turning Ratio - 60% Straight, 30% Right, 10% Left <-real world

## Slide 26: Approach: DQN Agent & Setting
Setting (Real-world data)
  Road network of Manhattan, multiplied volume of taxi data
  2510 traffic lights
Evaluation Metrics
  Travel time: Average travel time of all vehicles in the system - To evaluate the performance of the signal control method in transportation
  Throughput: the number of completed trips - If the throughput is high, indicates better control strategy

## Slide 27: Result
Performance Comparison
  Travel time is reduced 19.20% in MPLight over all other methods (second best time, config3)
  Throughput is increased 3% in MPLight over all other methods (second best time, config3)
Best performance compared to other RL method and Pressure control system(4x4)

## Slide 28: Result
Scalability Analysis
  Evaluate the method with other baselines under Manhattan, 2500 signalized intersection
  Compared to other methods, MPLight handle traffic signal more effectively and efficiently
Impact of Pressure-based Design(Manhattan)
  Evaluate the performance of RL-based method with and without ‘pressure’.

## Slide 29: Result & Conclusion
Impact of Parameter Sharing (Super Agent)
  Parameter sharing enables our model to converge faster  Effectiveness of parameter sharing
Conclusion
  Need more elaborate design for coordination and cooperation among neighboring intersection  MetaLight  Multi-agent learning(scalable)

## Slide 30: Comment
Improvement Proposal
  기존의 실험 구성
  논문과의 비교와 개선

## Slide 31: 현재 State와 Action, Reward 구성 방식
공통 주기: 90s (1 time step: 90s) - simulation Step: 1s - target update period: every 10 time steps(900s)
State
  Junction B1, B2의 lane별 정지한 차량의 수와 총 차량의 수 (B1: 30lanes, B2:28lanes)  Pressure Light
  lightMatrix: B1과 B2의 phase (3초 duration을 가진 phase data가 state로 존재하지 않음)
Action - Junction B2가 Agent  B2의 Phase Duration 조정
  phase1_duration: GGGGGggrrrrrrrGGGGGggrrrrrrr (Min: 20s, Max: 64s, yellow light:6s)
  phase2_duration: rrrrrrrGGGGGggrrrrrrrGGGGGgg
    Min duration과 Max duration이 존재하는 이유는 최소 유지 20초가 필요하기 때문
Junction B2

## Slide 32: 현재 State와 Action, Reward 구성 방식
Reward
  phase1_duration*0.1: phase1의 duration에 가점 부여  downstream에 reward 부여
  공통 주기 동안의 ‘B2B1’ edge와 ‘B1B0’ edge 차량 수 -> ‘B2B1’에서의 차량 수는 penalty -> ‘B1B0’에서의 차량 수는 reward  Pressure Light논문에서 Pressure =outflow-inflow
Target Update(10 timestep마다, hard update)
  1epoch 에서 40 time step부터 진행
  2 epoch부터는 10 time step마다 진행
B2B1
B1B0
Junction B2

## Slide 33: Training 구성 방식 제안(DQN 적용시)
Replay Save Time
  매 epoch당 Replay save Time을 뒤로 이동 - 現: 시작과 동시에 바로 진행 (replay는 1 time step마다 저장)  모든 차량이 교차로 내에서 대기할 수 있는 시점인 3 timestep 이상으로 조정
Target Update
  Learning Start Epoch 지정 (현재 90states/epoch가 replay에 저장) 現 replay: 40states가 저장됐을 때부터 target update  초반 학습의 Correlation 높음
  Learning Start 하는 Epoch를 4이상 (360 개의 data 기반 random sampling target update)
  Epoch 길이를 길게 (現:10000s/epoch -> 27000s/epoch이상)
  Soft target update로 변경

## Slide 34: Training 구성 방식 제안(종합)
Action
  10s/time step으로 조정 (MPLight)
  Penalty를 2 timesteps 미만 or 7 timesteps 이상 동일 신호 유지시 강력하게 부여 (state 에 포함)
  Action 구성이 만약 어렵다면 20s로 조정하고 4이상에서 penalty 부여
Reward
  Pressure based Reward system + CI(Critical Intersection)에서 중요 흐름에 가점 부여  CI에 가점을 주는 방식은 일반적인, 통용할 수 있는 방식이 아니므로 배제 가능
  모든 outflow에 Reward를 부여 (단, 우회전이 있는 lane은 직진과 우회전 필요)  Real world
State
  기존 교차로에서의 max phase score를 CNN으로 부분 filtering하여 받음 (3x3, 2 layers5x5 연동)  모든 내용을 공유하는 것이 아닌 부분만 공유  단점 Manhattan 처럼 직사각형인 경우만 유효한가? (실험에만 사용가능)
  인접데이터를 교차로 내의 모든 데이터를 받음 zero padding based  속도만 오를 가능성 높음
  1차, 3차선에 직좌, 직우 신호 포함 (우측은 항상 green)  현실성 높임

## Slide 35: Training 구성 방식 제안(알고리즘)
Remodeling
  MADDPG algorithm
    특징: continuous action space, Actor Critic
    Action을 3초에서 87초 사이의 continuous하게 구성해야 함
    Centralized Critic, Decentralized Actor
    Exploration Method가 infeasibility하다는 단점이 존재함
  QMIX based on hierarchical Q
    특징: 각 agent끼리 data 공유 x
    기존의 연동 시스템 단위 별 single-agent로 두고 mixing Q가 모든 Q를 종합해서 결과를 내림
    공통 Reward 설정을 기존의 Pressure로 진행하는게 의미가 없을 수 있음 (why? 한쪽의 pressure 감소가 다른 한쪽의 pressure 증가이므로)
  Dimensionality reduced RL
    Scalability에서 curse of dimensionality의 문제인 경우  dimension reduced by PCA
    IDDRL

## Slide 36: Thank you