## Slide 2: 목표
교통 공학 공부
SUMO Network 제작 TraCI 함수
State, Reward, Action 종류 판별
강화학습 내용 파악
논문 Review

## Slide 3: TOD

## Slide 4: SUMO Network 제작

## Slide 5: TraCI
Additional file 을 이용하여 Traffic Light를 조절 -.add.xml format 사용
Phase Setting - setPhase function
Duration Setting - setPhaseDuration
Complete Program Setting: Static signal Plan - setProgramLogic

## Slide 6: Defining New TLS-Programs
Additional file을 사용  tlLogic id를 부여하여 사용함(.nod.xml에서 부여한 id와 동일할 때, 동작함)
Program ID는 ‘off’를 제외하고 부여
아래 Character는 소문자는 decelerate 함을 의미(set할 때, 기준)
설명
Red Light, 이 신호일 때, junction에서 차량이 정지하면 Teleport
Yellow Light, 차량이 Junction에서 멀면 deceleration, 아니면 pass
Green Light with no priority, 비 보호 녹색 신호, 먼저 온 priority signal 수신 차량이 있는 경우 deceleration
Green Light with priority, junction을 우선 pass하는 신호
Green Right-turn arrow, junction type ‘traffic_light_right_on_red’에서만 생성되며, priority가 대향 방향 차량이 갖는 경우 정지
Red+yellow, Red에서 Green으로 바뀌기 전의 노란색 신호, 차량이 출발안함
깜박이면 차량이 양보해야함을 의미하는 신호
차량에게 통행권이 있는 신호

## Slide 7: Defining New TLS-Programs
TLS state 부여 방식 - 순서대로 부여하되, lane의 방향 별로 부여 - 0번에서 총 7가지 state가 존재
Junction 형태 설정시 개수 조절 가능
Connection 설정으로 Merge 형태 조절 가능
0
1
2
3

## Slide 8: Traffic State, Action
Traffic Lights Value Retrieval - ID list: getIDList - State: getRedYellowGreenState - Phase duration: getPhaseDuration, - Current phase: getPhase 함수, 현재 phase의 index - Complete program definition: getCompleteRedYellowGreenDefinition, TL 프로그램 받아오기
Change Traffic Lights State - Change state: setRedYellowGreenState - Change phase duration: setPhaseDuration - Complete program definition: setCompleteRedYellowGreenDefinition, 새로운TL 프로그램 삽입 - Change program logic: setProgramLogic : logic 삽입

## Slide 9: 현재 State와 Action, Reward 구성 방식
공통 주기: 90s (time step: 90초) - simulation Step: 1s - target update주기: 매 10 time step(900s)
State
  Junction B1, B2의 lane별 정지한 차량의 수와 총 차량의 수 (B1: 30lanes, B2:28lanes)  Pressure Light
  lightMatrix: B1과 B2의 phase (3초 duration을 가진 phase data가 state로 존재하지 않음)
Action - Junction B2가 Agent  B2의 Phase Duration 조정
  phase1_duration: GGGGGggrrrrrrrGGGGGggrrrrrrr (Min: 20s, Max: 64s, yellow light:6s)
  phase2_duration: GGGGGggrrrrrrrrGGGGGggrrrrrrrr

## Slide 10: 현재 State와 Action, Reward 구성 방식
Reward
  phase1_duration*0.1: phase1의 duration에 가점 부여
  공통 주기 동안의 ‘B2B1’ edge와 ‘B1B0’ edge 차량 수 -> ‘B2B1’에서의 차량 수는 penalty -> ‘B1B0’에서의 차량 수는 reward  Pressure Light의 Pressure 논문에서 outflow-inflow
B2B1
B1B0

## Slide 11: Training 구성 방식 제안
매 epoch당 Learning Start Time - 시작하자 마자 차량이 자리잡기 전의 데이터는 일반적이지 않음
Learning Start Epoch 지정 (현재 1epoch당 90개 state가 replay에 저장) 現 replay: 40 부터 target update  초반 학습의 Correlation 높음
  Learning Start 하는 Epoch를 4이상
  time step을 세분화 Action 형태 변화 필요
  Epoch 길이 길게 (現:10000s/epoch -> 27000s/epoch이상)
Learning 에서 augmentation(각 교차로에 대해서)

## Slide 12: Training 구성 방식 제안
차량 진입로를 줄이는 대신에 차량의 Random성을 주는 IDM controller와 가속도 분산 갖게 해서 차이를 줌
phase를 변화하는 action이 아닌 phase를 선택하게 하고 최소 시간은 20초로 하되, 최대 이상에서는 엄청난 penalty를 준다던지 하는 식으로 운용
phase 종류 수를 현재 8개 (논문상)에서 6개 내지는 4개로 줄임

## Slide 13: Toward A Thousand Lights: Decentralized Deep Reinforcement Learning for Large-scale Traffic Signal Control

## Slide 14: Motivation
Traffic congestion
  Led by rapid urbanization
  Increase harmful emissions (contributes 23% of total CO2 emission)  그 중에서 traffic에 의해 차지하는 양이 40%  Trend: applying RL method for traffic signal control
Traditional transportation approaches
  Pre-timed control
  Actuated control
  Adaptive control
  Optimization-based control  Given traffic model and pre-defined rule  Fail to adjust to dynamic traffic

## Slide 15: Motivation
Challenge
  To control and coordinate traffic lights in large-scale urban network  Highly correlated due to densely connected
  Traditional Method is not well adjusted when the traffic is dynamic
3 Key Issues to handle the challenge by RL method
  Scalability: learn effectively on a large scale, and the global optimization goal simultaneously
  Coordination: Optimizing signal timing for TL jointly when in close proximity
  Data feasibility: Not use the data that are hard to occur when learning by the RL-based method

## Slide 16: Related work
Conventional Transportation Methods for multi-intersection control
  Same cycle length
  Facilitated traffic of selected movement: modifying the offset between consecutive intersection  Problem of this approach
        Few network are only uniform for simple approach (Small grid network -> fixed offset achieve coordination)
        Difficult to provide a global optimization
Start from here
When arrive this point, turn on the green light

## Slide 17: Related work
Max Pressure : optimization-based method
  Providing global optimization through coordination
  Developed to optimize the global vehicle travel time, throughput and # of stops at intersections  Challenges
        Still rely on assumptions of simple traffic condition, HARD to apply to real world
RL-based single-intersection methods
  Outstanding performance over conventional transportation methods
  For satisfying scalability,  Advance to ‘RL-based multi-intersection methods’

## Slide 18: Related work
Reinforcement Learning(RL) based multi-intersection methods
  Treat all the intersection isolately and apply individual traffic signal control
    Scale-up easily
    Cannot coordinate with neighbors, achieve their own goals
  Centralized optimization over multiple coordinated agents
    Achieve coordination with neighbor intersections
    Network scale expands, optimization is infeasible due to large joint action space
 Trade-off between scalability and coordination

## Slide 19: Related work
Decentralized Approach based on RL
  Considering both scalability and coordination
Issues that are hard to apply RL in large-scale network
  Uni-intersection related reward system
  Few reward design for direct coordination
  Current RL method includes infeasible features in the states

## Slide 20: Approach
MPLight
  Utilizing simple features that are feasible in the real world <- overcome infeasibility
  Sharing parameters of intersections <- overcome scalability
    Not sharing all the parameters naively  inferior performance because of having different structures each
    Not applying the control of large flow to the system with little traffic - Following similar control logic and enhancing the speed of learning by sharing their learned knowledge - base model, ‘FRAP’
  Integrating the concept of “pressure” into reward design for coordination
    Derived from ‘max pressure control theory’, aimed at the global throughput in the area
    Balancing the distribution of vehicle by minimizing the pressure and maximizing the throughput - pressure: discrepancy of the number of vehicles inflow and outflow

## Slide 21: Approach: DQN Agent
Reinforcement Learning Structure(Deep Q-Network)
  Observation
    Current phase
    Pressure of the 12 traffic movements - fewer movements -> zero-padded
  Action(every 10s)
    Choose phase among the 8 candidate phases  Not choosing all the phase
    Select the phase based on Max Pressure Control Law
  Reward
    Difference between the sum of queueing vehicles inflows and the sum of queueing vehicles outflow  by maximizing the reward, agent will try to stabilizing
Super Agent
Agents

## Slide 22: Approach: DQN Agent & Setting
Parameter Sharing
  All parameters shared among all the agents  One intersection can get data from all the other intersections’ experience replay
Setting (Synthetic data on a 4x4 network)
  After the designated phase, 3s yellow signal and 2s all red time are followed
  Bi-directional and dynamic flows - Flat(=0.6) - Peak(=0.3)
  Turning Ratio - 60% Straight, 30% Right, 10% Left <-real world

## Slide 23: Approach: DQN Agent & Setting
Setting (Real-world data)
  Road network of Manhattan, multiplied volume of taxi data
  2510 traffic lights
Evaluation Metrics
  Travel time: Average travel time of all vehicles in the system - To evaluate the performance of the signal control method in transportation
  Throughput: the number of trips completed - If the throughput is high, indicates better control strategy

## Slide 24: Approach: FRAP
FRAP architecture(base model)
  Flipping and Rotation and considers All phase Configuration
  Focus on the relation between different traffic movement
    Reduction of exploration space by rotating and flipping
    Current model need 8phases experience to learn in the same state  By rotating, Reduces needed experience in ¼ scale

## Slide 25: Result

## Slide 26: Comment
네비게이션 시스템이 복잡? Why 애들이 차량이 많은 쪽위주로 열어주다보면 분명 개인 입장에서 기다리는 시간이 길 것으로 판단